M-Base, max. stroke 7000mm, stroke between 2250 and 7000mm optional in 100mm step for current, voltage and resistive output; stroke below 8000mm optional at will for pulse output.

Linearity for general ±0.1%FS; precision grade: ±0.05%～0.08%FS

Repeatability: 0.01%～0.02%FS for analog signal, 0.0025%～0.005%FS for digital output.

Signal output: current 2 wires 4～20mA, 3 wires 4～20mA;

Voltage 0～5Vdc or 0～10Vdc;

Resistive output 0～5kΩ or 0～10 kΩ;

Digital output: incremental or absolute encoder output;

Installation: bracket and fasten screw M4;

Life time: full stroke 106 reciprocating movement;

Protection grade: IP65

Note: for analog signal the sensing element is JAPAN made long-life potentiometer SAKAE brand. For encoder, by customers’ order.